## Slide 1: GEO-INFORMATICS Lecture # 2: Geospatial data capturing
Data Capturing Methods

## Slide 2: Data: The Fuel
The geographic data are information abut the earth’s surface and the objects are found on it.
Data are fuel to a GIS. How can we feed data such as map into a GIS?.
Data capture (collection) is the process of putting information into the system.
A wide variety of sources can be used for creating geographic data

## Slide 3: GIS Data Collection
Data collection is a time consuming, tedious, and expensive GIS activity.
  Typically it accounts for 15–50% of the total cost of a GIS project.
  If staff costs are excluded from a GIS budget, then in cash expenditure terms data collection can be as much as 60–85% of costs.
The processes of data collection are also referred to as data capture, data automation, data conversion, data transfer, data translation, and digitizing.

## Slide 4: Types and Sources of geographic data
Geographic data generally are available in two forms: analogue and digital data
Analogue data are physical product displaying information visually on paper, e.g. maps.
Digital data are information in a computer-readable form, e.g. satellite data.
There are various source for obtaining these type of data. These includes maps, aerial photographs, satellite images, existing tabular data (in analogue and digital format) and field data (GPS).
All of these sources can be grouped as primary or secondary sources

## Slide 5: Types and Sources of geographic data
Two main types of data sources are:
Primary data sources : Those collected in digital format specifically for use in a GIS project.
Secondary data sources: Digital and analog datasets that were originally captured for another purpose and need to be converted into a suitable digital format for use in a GIS project

## Slide 6: Types and Sources of geographic data

## Slide 7: Data capturing methods:
a) Vector data capture: This includes
  Keyboard entry, digitizing, field surveying,

## Slide 8: Keyboard entry
Involve reading or obtaining the coordinates of point features from maps or other source documents, typing the coordinates into a file in a tabular format, and reading the file into the GIS
In some GIS systems, point features are also called XY events
Used when the number of point features is small

## Slide 9: Digitizing
Involve choosing geographical features from the map or image, and manually tracing the features along their boundaries or shapes one by one using a digitizer while recording the coordinates of the points selected to approximate the boundary or shape of each feature
Tablet and on-screen digitizing

## Slide 10: Digitizing tablet

## Slide 11: On-screen digitizing
Scan the source document into a digital image if a paper map or aerial photo is used
Add the image into a GIS
Georeference the image
Trace features on the image using the mouse
Edit features
Add attribute data

## Slide 12: Typical digitizing errors

## Slide 13: Field surveying
Collect spatial data through direct measurements in the field
Traditionally, precision triangulation, trilateration, traversing and geometric levelling with plane tables, transits and theodolites
More recently, total stations and GNSS

## Slide 14: Raster data capture
Remotely sensed images, including satellite images and aerial photographs directly imported as raster data into GIS
Rasterisation: vector-to-raster conversion
Rasterisation: loss of information

## Slide 15: Crowdsourcing
Collect spatial data by soliciting contributions from the community or general public
•Involve the use of the Internet-enabled and location-aware mobile devices to gather location-specific information
•Three key technologies
•the Web, geotagging and mobile computing

## Slide 16: Activity:
Download OSM data (use: http://download.geofabrik.de/africa/tanzania.html (Use Qgis (exercise))
Download data from SDI and internet
Downloads satellite images: (use: https://earthexplorer.usgs.gov/)
Read and try these also: https://gisgeography.com/free-satellite-imagery-data-list/

## Slide 17: Spatial data transfer
Import existing digital spatial data from external sources
  may be in different data formats
  read directly, or
  translated into a suitable format

## Slide 18: Digital spatial data formats

## Slide 19: Spatial data transformation
Data structure conversion
Geometric transformation
Line simplification
Edge matching

## Slide 20: Spatial data editing
To remove the errors that arise during the encoding of spatial data
location errors
Topological errors
Attribute data errors

## Slide 21: Editing individual features

## Slide 22: Editing with topology rules

## Slide 23: Editing attribute data
Attribute data may contain observational or measurement errors, data entry errors or are simply out of date
Editing includes adding, deleting, or updating attributes associated with features and their values

## Slide 24
THANKS:
ANY QUESTION ??